## Slide 1: 7100 SW ISSUEs

## Slide 2
PW VXC Eth Port
PW VXC Eth Port
CEp
6/1
6/2
11/13
4/2
4/1
CEp
4/20
LAG
LAG
Test Center
12/4
9/7
interface xg
sub-interface switch vlan 300
Mpls Over Lag with vlan 150
interface tp-pw
sub-interface switch vlan 200
interface tp-pw
sub-interface switch vlan 200
Send: | DA | SA | 0x8100 | 300 | IP…
Receive: | DA | SA | 0x8100 | 200 | IP…
NE: 102
NE: 105
ISSUE1: The reason for PW VLAN ID not translated is ?
interface xg
sub-interface switch vlan 100
FP9.0: vlan-connection:
For VLAN cross-connection between MPLS-TP PW interface and external ethernet port,
the VID translation is only for direction from external port to PW interface in FP9.0.
@ page 367, Tellabs 7100® : Feature Package 9.0

## Slide 3
ISSUE2: Displayed the MACT Port name error
PW VXC Eth Port
14/1
6/1
14/2
6/2
Test Center
8/1
8/2
NE: 101
NE : 101
MAC over flexible oduF-1
Send | DA | SA | 0x88a8 | 666 | IP…
For bridge service(vlan), when ingress port and egress port doesn’t locate
at the same slot card. Displayed destination port of MACT is error.
show mac-address-table : dynamic unicast
Searching Mac Table - enter "no mac[-address-table]" to quit...
VcId VcName Vlan Mac Address Port Slot
-------------------------------------------------------------------
1 default 666 00:10:94:00:00:06 15/3 6
1 default 666 00:10:94:00:00:07 15/3 6
1 default 666 00:10:94:00:00:02 15/3 6
1 default 666 00:10:94:00:00:08 15/3 6
-------------------------------------------------------------------
show mac-address-table : dynamic unicast
Searching Mac Table - enter "no mac[-address-table]" to quit...
VcId VcName Vlan Mac Address Port Slot
-------------------------------------------------------------------
1 default 666 00:10:94:00:00:06 FL14/1/ODU2-2/ODUF-1 6
1 default 666 00:10:94:00:00:07 FL14/1/ODU2-2/ODUF-1 6
1 default 666 00:10:94:00:00:02 FL14/1/ODU2-2/ODUF-1 6
1 default 666 00:10:94:00:00:08 FL14/1/ODU2-2/ODUF-1 6
-------------------------------------------------------------------
Should be
Root cause: no distinction between local port and remote port at MACT Traverse function.
--------------------------------------------------------------------------------
Function: HAL_PktMacTableTraverseEntriesGetCallback()
mact.u.hal_if.physicalPortInterface.localPort = HAL_INTERFACE_PORT_GET(aradPort);
This is improper for remote port. It should use the HAL_INTERFACE_REMOTE_PORT_GET for remote port.
to be
Slot 6 MACT

## Slide 4
Vlan 30 (VSI)
Vlan 30 (VSI)
pnp
2/13
2/14
6/1
6/14
6/13
pnp
6/16
Test Center
8/1
8/2
TX | DA1 | SA1 | 0x8100 | 30 | IP…
NE: 101
NE: 104
ISSUE3:l2 bridge traffic recovery need to 5 mins when chaged a different port
Tx | DA2 | SA2 | 0x8100 | 30 | IP…
Create VSI (vlan 30 ) at NE 101 and NE 104
Add Port xg 2/13 , xg 6/1 in vsi vlan 30 at NE 101
Add Port xg 6/16 , xg 6/13 in vsi vlan 30 at NE 104
The packet with vlan 30 traffic is ok in two-way.
Packet Ethernet II format are DA1 = SA2, SA1 = DA2
4. remove ports xg 6/13 and 2/13 from their own vsi
and then add xg 6/14 and xg 2/14 in their vsi .
The packet with vlan 30 traffic is also delay.
MAC Table don’t update new ports instantly.
It needs 5 minutes aging time and then learn new ports.
Root cause:
when removing the port from VSI
, the related port learning-mac entries
in mact can’t be deleted.
Fix: Add new function in file vlanminp.c
FsMiVlanHwFlushPortandVlanandContext_adp
And call the new function to delete mact entries in VLANB_Npal.c.

## Slide 5
ISSUE4: ARP packets can’t be trapped to CPU on the MPLS compatible port.
PNP
2/6
6/1
Test Center
5/1
5/2
TX1 | DA1 | SA1 | 0x0806 | ARP…
NE: 101
CPU
Mpls Compatible port.
PVID: 4095
PNP port.
PVID: 1
X
TX2 | DA1 | SA1 | 0x0806 | ARP…
Create Port xg 1/6 as mpls compatible at NE 101
Create Port xg 2/6 as pnp port at NE 101
TC sends ARP packets to the two ports.
The arp packets can be trapped to cpu from PNP port.
However can’t be trapped to cpu from mpls compatible port.
5. Check the BCM Arad configure.
the packet with pvid 1 from PNP port can be sent to vsi 1.
the packet with pvid 4095 from mpls port can be sent to vsi 4095.
Root cause:
In Arad PMF, an existed PMF entry that qualifies the packets from VSI 4095 and its action is “drop”.
So the ARP packets on MPLS compatible port out from VSI 4095 will be dropped.
Solution:
1. Improve the priority of the trapped ARP PMF entry higher then the drop packets from VSI 4095 PMF entry.

## Slide 6
ISSUE5: there is a crash when testing RFC2544 with vlan-xc mode at mTera4.
4/3
7/1
NE: 104
RFC2544 Test enviroment:
Create vlan-xc between xg 1/7 and xg 4/3 at NE 104.
Create up meps at xg 7/1 NE 104 and xg 4/1 NE 103.
Run RFC2544 with initial 10G bps between up mep on xg 7/1 and xg 4/3.
The RFC2544 consists of Throughput, Latency and Loss frames test items. The Throughput and Latency tests are ok.
However there is a crash occurred when running the loss frame test in RFC2544.
Crash trace: a monitor task to read SFP status causes the crash.
FPGA looks abnormal work. (Detail information in attached crashed log).
Warm reboot can’t start up after system crash. It runs at initialized pcie3 and then reboot again. (Detail in attached warmreboot log).
6. Plug out and then plug in the line card, system starts up fine.
FPGA
4/3
NE: 103
FPGA
Up mep
Vlan-XC
Up mep
LBM/DMM
LBR/DMR
POCM-476 RFC2544: Frameloss report Partially Completed with VLAN XC mode
4/1
Up mep

## Slide 7
ISSUE6: L2.5 traffic blocked during warm reboot.
CEP:12/1
Test Center
5/1
5/2
NE: 100
Mpls Compatible port.
TX | DA1 | SA1 | 0x8100 | 100
PNP: 12/4
RX | DA | SA | 0x88A8 | 4000 | 8847
VSI: 1000
LER over MPLS compatible port 12/4
PW: outlabel:1000 inlabel:2000
Tunnel:outlabel:3000 inlabel:4000
During the line card warm reboot, no traffic sent out from xg 12/4
-------------------------------------------------------------------------------------------------------------
Debug: Compare the Arad configure between warm reboot and normal run stage.
NO | Normal stage | Warm reboot stage
1 | BCM.0> d chg IHP_VSI_LOW_CFG_2 1000 <FID_CLASS=7,DA_NOT_FOUND_DESTINATION=0x503e8> | BCM.0> d chg IHP_VSI_LOW_CFG_2 1000 <FID_CLASS=7,DA_NOT_FOUND_DESTINATION=0x1ffff>
2 | XG 12/4 [PNP port] STP status: Forwarding (STP Group) | XG 12/4 STP status: block (ingress and egress) BTW: PNP Ports in all STP group are blocked(ingress and egress) and CEP Ports are forwarding.
3 | There are two PMF entries to drop packets in egress. However they can’t take effect at normal stage | There are two PMF entries to drop packets in egress. One is to qualify the packet head flagged mc_learning_set. The other to qualify packets from ERP(system port: 164)

## Slide 8
ISSUE7: Flow Control can’t work between DIGI and Arad
Test Center
5/1
5/2
NE: 101
TX | DA1 | SA1 | 0x8100 | 100
When mass traffic to DIGI buffer of egress port , the DIGI drop pockets,
however no FC to ingress ports.
-------------------------------------------------------------------------------------------------------------
Arad
digi
Arad
digi
FC
FC
RX | x | x | x | x
Drop
Ingress doesn’t FC?

## Slide 9
Arad port | Inlaken0 | Arad port | Inlaken1
ucode_port_166 | ILKN0.176 | ucode_port_176 | ILKN1.176
ucode_port_167 | ILKN0.177 | ucode_port_177 | ILKN1.177
ucode_port_168 | ILKN0.178 | ucode_port_178 | ILKN1.178
ucode_port_169 | ILKN0.179 | ucode_port_179 | ILKN1.179
ucode_port_170 | ILKN0.180 | ucode_port_180 | ILKN1.180
ucode_port_171 | ILKN0.181 | ucode_port_181 | ILKN1.181
ucode_port_172 | ILKN0.182 | ucode_port_182 | ILKN1.182
ucode_port_173 | ILKN0.183 | ucode_port_183 | ILKN1.183
ucode_port_174 | ILKN0.184 | ucode_port_184 | ILKN1.184
ucode_port_175 | ILKN0.185 | ucode_port_185 | ILKN1.185
CFC_ILKN_RX_0_CAL | FC_INDEX | CFC_ILKN_RX_1_CAL | FC_INDEX
CFC_ILKN_RX_0_CAL.CFC0[1] | FC_INDEX=0xb8 | CFC_ILKN_RX_1_CAL.CFC0[1] | FC_INDEX=0xd0
CFC_ILKN_RX_0_CAL.CFC0[2] | FC_INDEX=0xb9 | CFC_ILKN_RX_1_CAL.CFC0[2] | FC_INDEX=0xd1
CFC_ILKN_RX_0_CAL.CFC0[3] | FC_INDEX=0xba | CFC_ILKN_RX_1_CAL.CFC0[3] | FC_INDEX=0xd2
CFC_ILKN_RX_0_CAL.CFC0[4] | FC_INDEX=0xbb | CFC_ILKN_RX_1_CAL.CFC0[4] | FC_INDEX=0xd3
CFC_ILKN_RX_0_CAL.CFC0[5] | FC_INDEX=0xbc | CFC_ILKN_RX_1_CAL.CFC0[5] | FC_INDEX=0xd4
CFC_ILKN_RX_0_CAL.CFC0[6] | FC_INDEX=0xbd | CFC_ILKN_RX_1_CAL.CFC0[6] | FC_INDEX=0xd5
CFC_ILKN_RX_0_CAL.CFC0[7] | FC_INDEX=0xbe | CFC_ILKN_RX_1_CAL.CFC0[7] | FC_INDEX=0xd6
CFC_ILKN_RX_0_CAL.CFC0[8] | FC_INDEX=0xbf | CFC_ILKN_RX_1_CAL.CFC0[8] | FC_INDEX=0xd7
CFC_ILKN_RX_0_CAL.CFC0[9] | FC_INDEX=0xc8 | CFC_ILKN_RX_1_CAL.CFC0[9] | FC_INDEX=0xd8
CFC_ILKN_RX_0_CAL.CFC0[10] | FC_INDEX=0xc9 | CFC_ILKN_RX_1_CAL.CFC0[10] | FC_INDEX=0xd9
Arad port | Base Q-Pair | Arad port | Base Q-Pair
ucode_port_166 | 184[0xb8] | ucode_port_176 | 208[0xd0]
ucode_port_167 | 185[0xb9] | ucode_port_177 | 209[0xd1]
ucode_port_168 | 186[0xba] | ucode_port_178 | 210[0xd2]
ucode_port_169 | 187[0xbb] | ucode_port_179 | 211[0xd3]
ucode_port_170 | 188[0xbc] | ucode_port_180 | 212[0xd4]
ucode_port_171 | 189[0xbd] | ucode_port_181 | 213[0xd5]
ucode_port_172 | 190[0xbe] | ucode_port_182 | 214[0xd6]
ucode_port_173 | 191[0xbf] | ucode_port_183 | 215[0xd7]
ucode_port_174 | 200[0xc8] | ucode_port_184 | 216[0xd8]
ucode_port_175 | 201[0xc9] | ucode_port_185 | 217[0xd9]

## Slide 10
ISSUE8: ERPS: Removing/Failing LAG link in ERPG causes "APSMNotReceived“
X
-------------------------------------------------------------------------------------------------------------
When the one member port in PO1 is down, it causes "APSMNotReceived“ in pear lc in ERPG.
Root cause: when lag port change, miss updating the mac tale of subring in ERPS.
Fix: Add the process ERPS_HW_SUB_RING_MC_UPDATE_NEEDED at function FsErpsHwRingConfig in erpsnp.c
POCM-3833

## Slide 11: Issue 9: Drop packet up to 25% at frame size from 64 to 77. however there is no issue when frame size is greater than 77.
The ETH frame generated by the JDSU (64 bytes length for example), can found that the IP Header Length (IHL) is increasing from 0x0 to 0xF. If the IHL set to bigger than 0xB, namely 0xC, 0xD, 0xE and 0xF, the minimum packet length ( DA(6)+SA(6)+TYPE(2)+IHL*4 + CRC(4) ) should be 66, 70, 74 and 78, but actually the ETH packet length is only 64 bytes in this case.
When chipset Arad check the IP header and verify the packet length, will find that the actual ETH frame length is smaller than the minimum, must be an invalid packet and just dropped it. So for 64 bytes packet generated by JDSU in this case, IHL with 0xC, 0xD, 0xE and 0xF will be dropped, IHL from 0x0 to 0xB will be OK, this is match the 25% packet drop rate.
Notes: The 64 -77 bytes packet dropped issue can be reproduced in shanghai lab and team found out the root cause. This issue can only be reproduced with JDSU analyzer(We use ONT 506 and seems you are using ONT 600), if use Spirent test center this issue never happen.
After investigation, it turned out that the packet drop is due to improper packet length.
If we look into the ETH frame generated by the JDSU (64 bytes length for example), can found that the IP Header Length (IHL) is increasing from 0x0 to 0xF. If the IHL set to bigger than 0xB, namely 0xC, 0xD, 0xE and 0xF, the minimum packet length ( DA(6)+SA(6)+TYPE(2)+IHL*4 + CRC(4) ) should be 66, 70, 74 and 78, but actually the ETH packet length is only 64 bytes in this case.
When chipset Arad check the IP header and verify the packet length, will find that the actual ETH frame length is smaller than the minimum, must be an invalid packet and just dropped it. So for 64 bytes packet generated by JDSU in this case, IHL with 0xC, 0xD, 0xE and 0xF will be dropped, IHL from 0x0 to 0xB will be OK, this is match the 25% packet drop rate.
If the packet length bigger or equal to the minimum packet length ,78 bytes, all the packet will pass the minimum packet length verification, so no packet dropped.
Also tried to manipulate the JDSU to have the IHL never bigger than 0xB when the packet length small than 78, also no packet drop happened.
With Spirent test center, we didn’t see packet generated with IHL bigger 0xB with default configuration for the same case.
For the JDSU tester seems we need to carefully manipulate the IP header to generate correct packets, maybe JDSU already have some configuration there to take care of this we just don’t know.

## Slide 12
Schedule template is ok.
VOQ QOS is ok

## Slide 13
There is a bug for forwarding the l2.5 traffic during the warm reboot.
The MPLS capably port should add in the stp group 63.
ISSUE6: L2.5 traffic blocked during warm reboot.

## Slide 14
the mac over odu2-1 interface can’t be up.
However mac over odu2-2 over the same port can be up.

## Slide 15
Create Vlan(bridge) and then delete the Vlan bridge . The inlif of bcm can’t be deleted.?